DAC Guidance Note: Theft of Metal and Use of Alternative Materials.

Given the frequency of repeated thefts, or attempted thefts, of lead roofing, the DAC is regularly approached for its view on the replacement of sheet lead and lead flashings with alternative products like stainless steel or felt-based systems. The Committee will consider a change from lead to another appropriate material but each case is considered individually by the Committee.

Encouragement will be given to alternative materials in the following circumstances:

- When such a change will have no detrimental historic or aesthetic impact.

- In visually discreet areas, like flat or shallow-pitched roofs concealed behind parapets.

- Where the roof is inconspicuous or of no historic importance.

- On ancillary structures of less significance than the main body of the church fabric; for example, on later modest vestry or porch additions.

- Where there have been multiple thefts within a short period of time.

On the other hand, the DAC favours like-for-like replacement of lead where this is possible. If a theft occurs, PCCs and their architects should consider the environmental and conservation benefits of replacing the lead before considering other materials less attractive to thieves. Lead is a sustainable material that can be easily cut and dressed to accommodate awkward details, provides reliable weather protection, and can easily be repaired in the event of local damage.

Where replacing lead is not possible, or would leave the building very vulnerable to repeated attacks, the Committee is of the opinion that alternative roofing material on shallow-pitched or flat roofs, is unlikely to be cheaper than lead and may even be more expensive.  Metal alternatives can look extremely good, and can be as long lasting as lead or slate, are almost impossible to remove, and have negligible scrap value. However, they can sometimes be noisy in inclement weather, and may be subject to technical problems concerning underside corrosion.

Felt-based roofing systems are short-lived and can be subject to maintenance problems. They may sometimes be acceptable on fairly modern or unlisted structures, but are completely unsuitable for historic buildings and extremely unlikely to receive approval from the DAC or the support of English Heritage, local authorities or the Amenity Societies. As a replacement for more traditional materials they are a very poor false economy.

Churches roofed in slate, tiles or other non-metallic materials are still likely to have large areas of lead flashings which can be very vulnerable. In some case it may be appropriate to replace stolen flashings with new reinforced mineral- or plastic-based materials, which can be dressed like lead, are suitably coloured and recyclable, and have no scrap value.

As soon as a theft occurs, contact your insurance company and Inspecting Architect immediately, and arrange to have the damaged area sheeted to prevent water ingress. Your architect will probably be able to suggest suitable people to do this. If you have the opportunity to take photographs of the damaged areas, these may prove useful later when making faculty applications and insurance claims.

When stolen metals are to be replaced like-for-like in the same materials, a faculty will still be required, but the Chancellor and the Archdeacons are prepared, in cases of real urgency, to give preliminary views in order to hasten the process.

Parishes must note that the ultimate responsibility for proposing any change from lead roofing to an alternative material must be taken following discussions with the Inspecting Architect to the church. On all Grade I and Grade II* buildings such changes will certainly require the support of English Heritage.

Like the DAC, English Heritage considers each individual case on its merits, and both have recently supported changing from lead to stainless steel alternatives on churches within the Diocese.

The Ecclesiastical Insurance Group issues an extremely useful Guidance Note on Theft of Metal which can be consulted at: www.ecclesiastical.com/theftofmetal

When the DAC grants permission for alternative materials to be used, it is with the intention that when the alternative material wears out, the parish reinstate the lead. As it is hoped that the demand for stolen lead will have stopped by the time the alternative materials wear out.